## Slide 1
z
x
y
DIGG
z
x
y
DEST

## Slide 2: Notes on Coordinate Systems*
Physical Cartesian coordinate system:
  Consensus definitions:
    O = mirror center / laser spot on mirror (equal?)
    Z = boresight
    Y = up
  Fluid definition:
    X = leftward (when looking with camera) – in accordance with right-hand rule convention
    X = rightward (when looking with camera) – in accordance with conventional 2D-images coordinate systems (as in Slide 1)
* told by Tal 30/4/19, summarized by Steve 1/5/19

## Slide 3: Notes on Coordinate Systems*
Mirror spherical coordinate system:
  Let N be the normal to the mirror, facing outward
  angX = angle between NZ and NX (measured from Z to X in X-Z plane)
  angY = angle between Ny and projection on X-Z plane (positive above plane)
  PZR’s measurements are converted to angX,angY in MC
Gen1 ES bug:
  Mirror rotated by 180° in installation, such that laser scanning goes from right-to-left instead of left-to-right
  Since Algo Pipe applies positive increments in X, output image is reversed (X = leftward, as in right-hand rule system) and requires back-reversion at the host
* told by Tal 30/4/19, summarized by Steve 1/5/19

## Slide 4: Notes on Coordinate Systems*
Image “pyramidal” coordinate system:
  Let B the boresight direction
  θy = angle between BZ and projection on Y-Z plane (positive above plane)
  θx = angle between BZ and projection on X-Z plane (measured from Z to X)
  For constant depth:
    Y is constant within row
    X is constant within column
    Observed plane together with receiver form a pyramid
  In general:
    θy = constant within row
    θx = constant within column
* told by Tal 30/4/19, summarized by Steve 1/5/19

## Slide 5: Notes on Coordinate Systems*
Pixel generation
  Laser is sensed by APD, but the image (based on ray directions) is attributed to the mirror
  Laser outward direction depends on the mirror’s normal and on inward direction (direction of intercepting the mirror – estimated in calibration process)
* told by Tal 30/4/19, summarized by Steve 1/5/19