## Slide 1: Algo Validation Metrics

## Slide 2: Metrics Interface
function [score, results] = metrics(frames, params)
frames =
1×100 struct array with fields:
z: 480x640 uint16
i: 480x640 uint16
c: 480x640 uint16
params =
struct with fields:
roi: 0.8
isRoiRect: 0
roiCropRect: 0.04
verbose: 1
camera: [1×1 struct]
0.8
0.04
0.04

## Slide 3: Metrics Interface: Results
function [score, results] = fillRate(frames, params)
score =
99.9295
res =
struct with fields:
frameFillRate: 99.9295
meanFillRate: 99.9314
stdFillRate: 0.0217
score: 'frameFillRate'
units: 'percentage'
error: 0

## Slide 4: Metrics: LOS Grid Drift
Check how the checkboard corners move over time
  Detect checkboard
  Use linear fit of the corners x’s and y’s to measure drift
meanStdX: 0.3621
meanStdY: 0.1345
meanDriftX: 0.6088
meanDriftY: 0.0568
maxDriftX: 0.9846
maxDriftY: 0.2847
score: 'maxDriftX'
units: 'pixels'

## Slide 5: Metrics: LOS FOV and Laser Drift
Check how FOV and Laser ON/OFF move over time
  Detect FOV and Nest boundaries
  Use linear fit to measure drift
stdFovL: 0.2043
stdFovR: 0.5291
stdFovT: 0.1291
stdFovB: 0.1490
stdLdOnL: 0.2514
stdLdOnR: 0.5356
stdLdOnT: 0.1563
stdLdOnB: 0.1541
driftFovL: 0.0802
driftFovR: -1.3084
driftFovT: 0.0191
driftFovB: 0.1201
driftLdOnL: -0.1796
driftLdOnR: -1.2650
driftLdOnT: 0.1133
driftLdOnB: 0.0437
score: 'driftLdOnL'
units: 'pixels'

## Slide 6: Metrics: PlaneFit (zStd)
Check how far the points of the wall from the fit plane
  Fit plane for every frame
  Measure distances (z only) from the plane
score =
3.3555
res =
struct with fields:
rmsPlaneFitDist: 3.3555
maxPlaneFitDist: 13.7116
score: 'rmsPlaneFitDist'
units: 'mm'
error: 0

## Slide 7: Metrics: Grid Inter Distances (Alex’s error)
Check how far the distances between all possible corners in 3D from the real distances
  Unproject corners into 3D
  Compare the distances
score =
2.0547
res =
struct with fields:
meanError: 2.0547
rmsError: 2.5894
score: 'meanError'
units: 'mm'
error: 0

## Slide 8: Metrics: Grid Edge Sharpness
Check how sharp the edges of the grid
  Find the checkboard
  Measure the width of the edges
score =
2.1709
res =
struct with fields:
gridSize: [9 13]
points: [117×2 double]
horizMin: 1.8635
horizMax: 2.5828
horizMean: 2.1709
horizStd: 0.1772
vertMin: 1.8842
vertMax: 3.7097
vertMean: 2.4070
vertStd: 0.3450
meanFrame: [1×1 struct]
score: 'horizMean'
units: 'pixels'
error: 0